## Slide 1: SBFT Introduction
Instructor: Julio Gutierrez

## Slide 2: Agenda:
Topic: | Duration:
Functional Test Introduction | 5 min
SBFT introduction | 5 min
Types of SBFT | 15 min
Readout Results | 15 min
High Level SBFT Test Flow | 15 min
Q & A | 5

## Slide 3: Functional Test Introduction
What is a functional test?
  “Functional testing verifies device architecture; its coverage occurs when signal paths are exercised and correct functional behavior occurs”
Test writing flow
Some DFTs used for test writing:
  ATM, TAM, MailBox, WDAR, DDR Read/Return, etc.
MAX FILE
Built Test
Assembly test
Deploy format:
ASM
OBJ
LDAT
VAULT + TVPV
Machine Readable
Human Readable
TESTER
Libraries

## Slide 4: SBFT Introduction
What is SBFT?
  The acronym stands for Structural Base Functional Test, it refers to a test method that enables application of at-speed functional test on low-pin-count structural tester.

## Slide 5: SBFT content types
Core Coverage:
  SBFT MLC
    Functional test is loaded into MLC memory
    Cores are isolated to prevent a failing core from interfering with the other cores
    Capability for parallel testing
    High reusability across products.
Functional Test
MLC Test
MLC Test

## Slide 6: SBFT content types
Core Coverage:
  SBFT LLC
    Functional test is loaded into LLC memory
    Tile/Slice are isolated to prevent a failing Tile/Slice from interfering with the other cores
    Capability for parallel testing
    High reusability across products.
Functional Test
LLC Test

## Slide 7: SBFT content types
Uncore Coverage:
  SBFT FCX (Full Chip) (CLR/IIO/QPIs/MCs)
    Portions of the Functional test is loaded into all the LLCs
    DUT is configured to enable specific sections .
    Single Test execution.
    Only two cores enable to execute the test.
    Content is Product/Chop specific content.
Functional Test
FCX Test 1/6
FCX Test 2/6
FCX Test 3/6
FCX Test 4/6
FCX Test 5/6
FCX Test 6/6

## Slide 8: SBFT content types
Uncore Coverage:
  SBFT MOFC (Mesh Only Full Chip):
    Same test is loaded across all LLCs.
    Communication across all the tiles is enable
    Test is self adaptive to core count changes since all the information leaves on all tiles.
    Content is Product specific content.
Functional Test
MOFC Test

## Slide 9: SBFT Results
Architectural Results.
  Thread Status Check.
    Check is the core completed the test successfully and reach the HALT instruction.
  Performance Monitor Counters.
    Core registers which can be configured to count certain events; e.g.
      # micro-ops retired
      # macro-ops
      # cache misses
    Hard to predict the results without simulation
  Explicit Register Results.
    Counters and registers can be combined to have a more robust result.
    Expected result is provided by the test writer and typically is ACED.

## Slide 10: SBFT Results
Signature Results
  Signature
    Based on Scan cells inserted across the device.
    There are many scanout chains throughout the CPU that are collected in scubs (scanout FUB = Functional Unit Block )
    Linear Feedback shift register (LFSR): is a shift register whose input bit is a linear function of its previous state.
    Adds visibility to the internal status of the device.
    Requires very stable initial state (no X’s)
    Masking can be executed by scan cell, scan chain or SCUB depending on the product.

## Slide 11: Scanout Scub loop Block Diagram

## Slide 12: SBFT Results
Signature Results:
  Self_Signature:
    This is a DFT where we use a core to determine if other cores have passed or failed the test.
    It requires a set-up of a reference core
    Expected result are logical lows since it is based on XORs.

## Slide 13: High Level SBFT Test Flow
Reset
  Generic CPU bring-up
    Fuse config:
      Core enabling
      Cache repair
      Ratios
    PLL trim/lock
    Core reset
    PCU stall
    Set I/O’s to known state
    MCI/NTI/STF configuration
    FIVR settings

## Slide 14: High Level SBFT Test Flow
Setup Segment 130/Precat
  Isolation of the sub_section of the device
  Mapping of the caches (Saving a section for the CleanX)
  Loading of the cleanX
  Core reset

## Slide 15: High Level SBFT Test Flow
Load
  CleanX execution starts through MBP Read CleanX results
  Mapping of the caches (avoiding section where CleanX is loaded)
  Core reset
  Load the test into caches (CPL)

## Slide 16: High Level SBFT Test Flow
Execute
  Execution flag through MBP
  Wait for test to finish execution:
    Wait time cycles are idle state
    Divided in the Main Memory and Subroutine Memory to be “ratio agnostic”
  Some product include an end of test pulse trigger by the Halt instruction in the core to ensure test completed and speed up the wait time fine tuning.

## Slide 17: High Level SBFT Test Flow
Unload
  Thread Status check
  Read out self check results
  Read out performance monitor results
  Read out Signature

## Slide 18: Expected Bins
Bin 44
  General SBFT Bin for FG content
Bin 45
  Searches

## Slide 19: Reference information
ITMH