## Slide 1
IDSK
Intra Die Statistical Kill
SBFT - MPE

## Slide 2: Intra Die Statistical Kill (IDSK)
This infrastructure measures Intra die core performance and performs defeature once an outlier core has been identified.
It is a statistical method used to analyze the performance between cores based on the Vmin behavior per core, to establish a core disablement.

## Slide 3
Once Vmin distribution per core is acquired, IDSK test computes the mean value, the covariance, the standard deviation and the Z-score for each core.
Tagging the ones with a given delta from mean and updating valid core tracking structure and disabling possible bad cores

## Slide 4: Z-score and Vmin Delta
Equation 2. Vmin Delta Calculation
Equation 1. Z-score Calculation

## Slide 5
Structural defects can be pointed using this software solution since it detects the cores that may not necessarily fail in the tests (patterns) but are outliers of the Vmin distribution.

## Slide 6: IDSK instance parameters
Parameter Name | Required? | Type | Comments
VminInput | Yes | String | Incoming VMIN string
OutlierVector | Yes | String | Outgoing tracking structure GSDS
BitLogic | Yes | Choice | Kill for zscore AND/OR vmin_delta. Values are AND(Default) or OR
StdDevFloor | Yes | Double | Minimum standard deviation allowed
StdDevCeiling | Yes | Double | Maximum standard deviation allowed
ZscoreLimit | Yes | Double | Sigma kill limit
VminDelta | Yes | Double | Maximum vmin difference allowed

## Slide 8: Data log output
Data | Description
Mean | Mean of all valid Vmin values provided
Standard Deviation | Std deviation parameter calculated in idsk test
Standard Deviation Fixed | Std deviation after user provided Ceiling and Floor are applied
IDSK Cores to Kill | IDSK cores identified to be defeatured in the tracking structure (different from the XOR between the incoming core configuration and the outlier cores identified)
InputVminValues | All vmin values provided (not just valid ones)
Median | Median value for all the enabled cores
Max | Highest Vmin core value from all the enabled cores
Min | Lowest Vmin core value from all the enabled cores
FlagForOutliers | 1 if outlier was detected 0 if no outliers were detected

## Slide 9: Data log output
Mean | standardDeviation | standardDeviationFixed |
IDSK Cores to Kill | InputVminValues | Median | Max | Min | FlagForOutliers
Example:
0.8605|0.0109|0.0109|
00000000000000000000001000000000000000000000|
0.855,0.863,0.873,0.868,0.86,0.865,0.85,0.863,0.863,0.853,0.86,0.86,0.875,0.85,0.865,0.843,0.863,0.858,0.855,0.843,0.858,0.86,0.912,0.855,0.853,0.855,0.868,0.863,0.855,0.858,0.855,0.853,0.873,0.853,0.85,0.863,0.873,0.87,0.86,0.863,0.868,0.853,0.858,0.85|
0.86|0.912|0.843|1
TestResult:b00000000000000000000001000000000000000000000|Incoming:b00000000000000000000000000000000000000000000|Outgoing:b00000000000000000000000000000000000000000000

## Slide 10: Exit Ports
Exit Port | Condition | Description
-2 | Alarm | Any alarm condition
-1 | Error | Any software condition error
0 | Fail | Failing condition
1 | Pass | Passing condition

## Slide 11: Script analysis

## Slide 12: Script analysis

## Slide 13: QA failure example
QA failure:
74YU559700150 | U5 | FUN_COREDRG_COMP::COREDRG_CORE_VMIN_K_SRHAVX2F7_STF_CORE_VMIN_F7_DRAGONMLCMTT_7912::CORETracking | TestResult:b00000000000000000000001000000000000000000000¦ Incoming:b00000000001000000000000000000000000000000000¦ Outgoing:b00000000001000000000001000000000000000000000
IDSK results:
74YU559700150 | FUN_COREDRG_COMP::COREDRG_CORE_VMIN_K_CHKAVX3F7_STF_CORE_VMIN_F7_IDSKU5 | 0.8605¦0.0109¦0.0109¦00000000000000000000001000000000000000000000¦0.855,0.863,0.873,0.868,0.86,0.865,0.85,0.863,0.863,0.853,0.86,0.86,0.875,0.85,0.865,0.843,0.863,0.858,0.855,0.843,0.858,0.86,0.912,0.855,0.853,0.855,0.868,0.863,0.855,0.858,0.855,0.853,0.873,0.853,0.85,0.863,0.873,0.87,0.86,0.863,0.868,0.853,0.858,0.85¦0.86¦0.912¦0.843¦1

## Slide 14: Useful links: https://dev.azure.com/mit-us/PrimeWiki/_wiki/wikis/PrimeWiki.wiki/99519/Idsk