## Slide 1: Tap Link Training for 10nm
Enrique Santillan

## Slide 2: Basic Tap Link Cluster
CMDs
SCANI: 0010
SCAND: 0011101
SCANI: 0001
SCAND: 0101001
Stage:
POWER ON
Reset
Inputs IR
Inputs DR
Inputs IR
Inputs DR

## Slide 3: Diff with Legacy Tap (BDX-SKX)
Legacy Tap:
  IR: (UNCOREIR)+(COREIR)
  DR: <DATA TO SEND>
Example:
  #SA_TAPCONFIG
  p1_scani: 'b00111000011111111 ;
  p1_to_state: Run-Test/Idle ;
  #SA.TAPCONFIG[32] + PAD[1] = 33 bits
  p1_scand: 10000000000000000000000000001000_0 , XXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXX ;
  # CORE_IDVRESET
  p1_scani: 'b11111111101101001 ;
  p1_to_state: Run-Test/Idle ;
  # PAD[1] + PAD[2] + CORE0.IDVRESET[1] + PAD[2] + PAD[1] = 7 bits
  p1_scand: 000_0_000 , XXXXXXX ;
Tap Link:
CLTAP:
  IR: CLTAPIR
  DR: <DATA TO SEND>
Agent:
  IR: CLTAP TO AGENT IR
  DR: AGENT IR
  IR: CLTAP TO AGENT DR
  DR: <DATA TO SEND>
  Agent: (CORE_TAPCONFIG)
    scani: 001111001100 ;
    to_state: Run-Test/Idle ;
    scand: 01010010, XXXXXXXX ;
    to_state: Run-Test/Idle ;
    scani: 001111001101 ;
    to_state: Run-Test/Idle ;
    scand: 0111000000000000000110010010011100000000000000, XXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXX ;
Examples:
  CLTAP:
    #CLTAP TAP CONFIG
    scani: 000011000100 ;
    to_state: Run-Test/Idle ;
    scand: 0100, XXXX ;
    to_state: Run-Test/Idle ;

## Slide 4: Legacy Tap (BDX)
Legacy Tap:
  IR: (UNCOREIR)+(COREIR)
  DR: <DATA TO SEND>
Example:
  #SA_TAPCONFIG
  p1_scani: 'b00111000011111111 ;
  p1_to_state: Run-Test/Idle ;
  #SA.TAPCONFIG[32] + PAD[1] = 33 bits
  p1_scand: 10000000000000000000000000001000_0 , XXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXX ;
  # CORE_IDVRESET
  p1_scani: 'b11111111101101001 ;
  p1_to_state: Run-Test/Idle ;
  # PAD[1] + PAD[2] + CORE0.IDVRESET[1] + PAD[2] + PAD[1] = 7 bits
  p1_scand: 000_0_000 , XXXXXXX ;
Listen to bits[16:8]
Listen to bits[7:0]

## Slide 5: Tap Link (CNL-ICXSP-KNH)
Tap Link:
CLTAP:
  IR: CLTAPIR
  DR: <DATA TO SEND>
Agent:
  IR: CLTAP TO AGENT IR
  DR: AGENT IR
  IR: CLTAP TO AGENT DR
  DR: <DATA TO SEND>
  Agent: (CORE_TAPCONFIG)
    scani: 001111001100 ;
    to_state: Run-Test/Idle ;
    scand: 01010010, XXXXXXXX ;
    to_state: Run-Test/Idle ;
    scani: 001111001101 ;
    to_state: Run-Test/Idle ;
    scand: 0111000000000000000110010010011100000000000000, XXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXX ;

## Slide 6: What’s inside a tap Glue agent.
3 ways to assert the IR GLUE valid:
Match the pre-programed local address.
Match the pre-programed global address.
Match the configurable address.
Each GLUE agent has 2 IR registers:
  Configuration.
    Configurable addrs.
    Disable the agent.
    Disable the output.
    ….
  Status.
    Agent has PWR GOOD?
    Agent is connected?
    …

## Slide 7: Config and Status registers per agent
TAP CONFIG
DYNAMIC_WR_EN
DYNAMIC_BASE_ADDRESS
DISABLE_WR_EN
DISABLE_TDO
DISABLE_PREVIOUS_LINK_TDO
DISABLE_TAP
PWRGOOD_OVERRIDE_EN
PWRGOOD_OVERRIDE_VALUE
PHYSICAL_OFFSET_SEL_WE_EN
PHYSICAL_OFFSET_SEL
MODE_WR_EN
SHIFTDR_MODIFY_SET
SHIFTDR_MODIFY_CLEAR
DISABLE_UPDATEDR
DISABLE_CAPTUREDR
TAP STATUS
EP_LOGIC_EXIST
DYNAMIC_BASE_OPCODE
FSM_ERROR
ACCESS_ON_PWR_NOT_GOOD
TARGET_IP_PWRGOOD_STATUS
DISABLED_TAP

## Slide 8: IR/DR protocol example
For example if we have IP2 TAP with 8bits instruction register and we want to drive the following IR/DR
IR 0x5f (8 bits)
DR 0x3 (4 bits DR)
IP2 TAP Link Base Address (LBA) is 0x40:
TAP IP2 link IR opcode 0x40
TAP IP2 link DR opcode 0x41
Note that IP IR opcode are not overlapping with any of the TAP IPs on the network
0x41
0x41
0x41
0x41
0x5f
0x3
0x40
0x40
0x40
0x40
LBA=0x3C
LBA=0x40
LBA=0x44
IR 0x40 (IP2 linkIr)
DR
IR 0x41 (IP2 linkDr)
DR
IR
0x5f
DR
0x3
0x41
0x5f
0x3
T

## Slide 9: Info from the model:
TAP_GLUE stap_core_core_core_c0_r1_EP {
OPCODES {
// NAME : ENCODING : LAYOUT
stap_core_core_core_c0_r1_IR : 'b01001110110100 : %LINK_IR ;
stap_core_core_core_c0_r1_DR : 'b01001110110101 : %LINK_DR ;
stap_core_core_core_c0_r1_TL_CFG : 'b01001110110110 : %LINK_CFG ;
stap_core_core_core_c0_r1_TL_STATUS : 'b01001110110111 : %LINK_STATUS ;
ALL_CORE_TAPS_3444_PARIR : 'b11010001000100 : %LINK_PAR_IR ;
ALL_CORE_TAPS_3444_PARDR : 'b11010001000101 : %LINK_PAR_DR ;
} // OPCODES
PADDING {
// NAME : PADDING
stap_core_core_core_c0_r1_IR : 2'b00 + DATA;
stap_core_core_core_c0_r1_DR : 1'b0 + DATA + 22'b0000000000000000000000;
stap_core_core_core_c0_r1_TL_CFG : DATA + 22'b0000000000000000000000;
stap_core_core_core_c0_r1_TL_STATUS : DATA + 22'b0000000000000000000000;
ALL_CORE_TAPS_3444_PARIR : 2'b00 + DATA;
ALL_CORE_TAPS_3444_PARDR : 1'b0 + DATA + 22'b0000000000000000000000;
} // PADDING
TAP stap_core_core_core_c0_r1 {
@IRSIZE = 8;
@TAPLINK_NETWORK_REGS = "CLTAP,taplink_dfx_glb_CFG,taplink_chn_h0_CFG,taplink_chn_vcore_011_CFG,taplink_chn_corenotch_c0_r1_CFG,taplink_core_c0_r1_CFG";
@TAPLINK_NETWORK_TREE = "CLTAP[0L],taplink_dfx_glb[0L],taplink_chn_h0[4L],taplink_chn_vcore_011[1L],taplink_chn_corenotch_c0_r1[0L],taplink_core_c0_r1[1T]";
@TAPLINK_TAPPARENTNAME = "taplink_core_c0_r1";
@TAPLINK_TAPPARENTPORTINDEX = "1";
OPCODES {
// NAME : ENCODING : LAYOUT
CORE_ALLCLKDIS : 'b00010100 : CORE_ALLCLKDIS ;
CORE_ALLCLKEN : 'b00010101 : CORE_ALLCLKEN ;
CORE_ALTRESETVEC : 'b00010110 : CORE_ALTRESETVEC ;
CORE_BRKPTCTL0 : 'b00010111 : CORE_BRKPTCTL0 ;
CORE_BRKPTCTL1 : 'b00011000 : CORE_BRKPTCTL1 ;
CORE_BRKPTCTL2 : 'b00011001 : CORE_BRKPTCTL2 ;
CORE_BRKPTCTL3 : 'b00011010 : CORE_BRKPTCTL3 ;
CORE_BRKPTCTL4 : 'b00011011 : CORE_BRKPTCTL4 ;
CORE_BRKPTCTL5 : 'b00011100 : CORE_BRKPTCTL5 ;
CORE_BRKPTEN0 : 'b00011101 : CORE_BRKPTEN0 ;
CORE_BRKPTEN1 : 'b00011110 : CORE_BRKPTEN1 ;
CORE_BRKPTEN0 {
@SIZE = 1;
@DESCRIPTION = "CORE_BRKPTEN0 register";
@RDL_TAPISDRREMOTE = "false";
@RDL_TAPOPCODESECURITYLEVEL = "SECURE_GREEN";
ALIASES {
DR_ENABLE {
@DESCRIPTION = "test";
@ACCESSTYPE = "RW/V";
@RDL_TAPPRISIGNAL = "ComShiftRegT731H[0:0])";
@RDL_TAPSHADOWSIGNAL = "CORE_BRKPTEN0_RegMnnnH.DR.ENABLE)";
} [0:0];
} // ALIASES
} // REGISTER CORE_BRKPTEN0

## Slide 10: Example:
From the above specs write a IR/DR sequence for a write to the core_BrkEn0 = 1
  1st Get the agent IR address:
    0x01001110110100
  2nd Get the IR Opcode:
    0x00011101
  3rd Get the IR padding:
    2b0
  4th Get the agent DR address:
    0x01001110110101
  5th Form the IR Data chain
    0x1
  6th Get the DR padding:
    1b0 + 22b0
TAP_GLUE stap_core_core_core_c0_r1_EP {
OPCODES {
// NAME : ENCODING : LAYOUT
stap_core_core_core_c0_r1_IR : 'b01001110110100 : %LINK_IR ;
stap_core_core_core_c0_r1_DR : 'b01001110110101 : %LINK_DR ;
stap_core_core_core_c0_r1_TL_CFG : 'b01001110110110 : %LINK_CFG ;
stap_core_core_core_c0_r1_TL_STATUS : 'b01001110110111 : %LINK_STATUS ;
ALL_CORE_TAPS_3444_PARIR : 'b11010001000100 : %LINK_PAR_IR ;
ALL_CORE_TAPS_3444_PARDR : 'b11010001000101 : %LINK_PAR_DR ;
} // OPCODES
PADDING {
// NAME : PADDING
stap_core_core_core_c0_r1_IR : 2'b00 + DATA;
stap_core_core_core_c0_r1_DR : 1'b0 + DATA + 22'b0000000000000000000000;
stap_core_core_core_c0_r1_TL_CFG : DATA + 22'b0000000000000000000000;
stap_core_core_core_c0_r1_TL_STATUS : DATA + 22'b0000000000000000000000;
ALL_CORE_TAPS_3444_PARIR : 2'b00 + DATA;
ALL_CORE_TAPS_3444_PARDR : 1'b0 + DATA + 22'b0000000000000000000000;
} // PADDING
TAP stap_core_core_core_c0_r1 {
@IRSIZE = 8;
@TAPLINK_NETWORK_REGS = "CLTAP,taplink_dfx_glb_CFG,taplink_chn_h0_CFG,taplink_chn_vcore_011_CFG,taplink_chn_corenotch_c0_r1_CFG,taplink_core_c0_r1_CFG";
@TAPLINK_NETWORK_TREE = "CLTAP[0L],taplink_dfx_glb[0L],taplink_chn_h0[4L],taplink_chn_vcore_011[1L],taplink_chn_corenotch_c0_r1[0L],taplink_core_c0_r1[1T]";
@TAPLINK_TAPPARENTNAME = "taplink_core_c0_r1";
@TAPLINK_TAPPARENTPORTINDEX = "1";
OPCODES {
// NAME : ENCODING : LAYOUT
CORE_ALLCLKDIS : 'b00010100 : CORE_ALLCLKDIS ;
CORE_ALLCLKEN : 'b00010101 : CORE_ALLCLKEN ;
CORE_ALTRESETVEC : 'b00010110 : CORE_ALTRESETVEC ;
CORE_BRKPTCTL0 : 'b00010111 : CORE_BRKPTCTL0 ;
CORE_BRKPTCTL1 : 'b00011000 : CORE_BRKPTCTL1 ;
CORE_BRKPTCTL2 : 'b00011001 : CORE_BRKPTCTL2 ;
CORE_BRKPTCTL3 : 'b00011010 : CORE_BRKPTCTL3 ;
CORE_BRKPTCTL4 : 'b00011011 : CORE_BRKPTCTL4 ;
CORE_BRKPTCTL5 : 'b00011100 : CORE_BRKPTCTL5 ;
CORE_BRKPTEN0 : 'b00011101 : CORE_BRKPTEN0 ;
CORE_BRKPTEN1 : 'b00011110 : CORE_BRKPTEN1 ;
TAP_GLUE stap_core_core_core_c0_r1_EP {
OPCODES {
// NAME : ENCODING : LAYOUT
stap_core_core_core_c0_r1_IR : 'b01001110110100 : %LINK_IR ;
stap_core_core_core_c0_r1_DR : 'b01001110110101 : %LINK_DR ;
stap_core_core_core_c0_r1_TL_CFG : 'b01001110110110 : %LINK_CFG ;
stap_core_core_core_c0_r1_TL_STATUS : 'b01001110110111 : %LINK_STATUS ;
ALL_CORE_TAPS_3444_PARIR : 'b11010001000100 : %LINK_PAR_IR ;
ALL_CORE_TAPS_3444_PARDR : 'b11010001000101 : %LINK_PAR_DR ;
} // OPCODES
PADDING {
// NAME : PADDING
stap_core_core_core_c0_r1_IR : 2'b00 + DATA;
stap_core_core_core_c0_r1_DR : 1'b0 + DATA + 22'b0000000000000000000000;
stap_core_core_core_c0_r1_TL_CFG : DATA + 22'b0000000000000000000000;
stap_core_core_core_c0_r1_TL_STATUS : DATA + 22'b0000000000000000000000;
ALL_CORE_TAPS_3444_PARIR : 2'b00 + DATA;
ALL_CORE_TAPS_3444_PARDR : 1'b0 + DATA + 22'b0000000000000000000000;
} // PADDING
TAP_GLUE stap_core_core_core_c0_r1_EP {
OPCODES {
// NAME : ENCODING : LAYOUT
stap_core_core_core_c0_r1_IR : 'b01001110110100 : %LINK_IR ;
stap_core_core_core_c0_r1_DR : 'b01001110110101 : %LINK_DR ;
stap_core_core_core_c0_r1_TL_CFG : 'b01001110110110 : %LINK_CFG ;
stap_core_core_core_c0_r1_TL_STATUS : 'b01001110110111 : %LINK_STATUS ;
ALL_CORE_TAPS_3444_PARIR : 'b11010001000100 : %LINK_PAR_IR ;
ALL_CORE_TAPS_3444_PARDR : 'b11010001000101 : %LINK_PAR_DR ;
} // OPCODES
PADDING {
// NAME : PADDING
stap_core_core_core_c0_r1_IR : 2'b00 + DATA;
stap_core_core_core_c0_r1_DR : 1'b0 + DATA + 22'b0000000000000000000000;
stap_core_core_core_c0_r1_TL_CFG : DATA + 22'b0000000000000000000000;
stap_core_core_core_c0_r1_TL_STATUS : DATA + 22'b0000000000000000000000;
ALL_CORE_TAPS_3444_PARIR : 2'b00 + DATA;
ALL_CORE_TAPS_3444_PARDR : 1'b0 + DATA + 22'b0000000000000000000000;
} // PADDING
CORE_BRKPTEN0 {
@SIZE = 1;
@DESCRIPTION = "CORE_BRKPTEN0 register";
@RDL_TAPISDRREMOTE = "false";
@RDL_TAPOPCODESECURITYLEVEL = "SECURE_GREEN";
ALIASES {
DR_ENABLE {
@DESCRIPTION = "test";
@ACCESSTYPE = "RW/V";
@RDL_TAPPRISIGNAL = "ComShiftRegT731H[0:0])";
@RDL_TAPSHADOWSIGNAL = "CORE_BRKPTEN0_RegMnnnH.DR.ENABLE)";
} [0:0];
} // ALIASES
} // REGISTER CORE_BRKPTEN0
TAP_GLUE stap_core_core_core_c0_r1_EP {
OPCODES {
// NAME : ENCODING : LAYOUT
stap_core_core_core_c0_r1_IR : 'b01001110110100 : %LINK_IR ;
stap_core_core_core_c0_r1_DR : 'b01001110110101 : %LINK_DR ;
stap_core_core_core_c0_r1_TL_CFG : 'b01001110110110 : %LINK_CFG ;
stap_core_core_core_c0_r1_TL_STATUS : 'b01001110110111 : %LINK_STATUS ;
ALL_CORE_TAPS_3444_PARIR : 'b11010001000100 : %LINK_PAR_IR ;
ALL_CORE_TAPS_3444_PARDR : 'b11010001000101 : %LINK_PAR_DR ;
} // OPCODES
PADDING {
// NAME : PADDING
stap_core_core_core_c0_r1_IR : 2'b00 + DATA;
stap_core_core_core_c0_r1_DR : 1'b0 + DATA + 22'b0000000000000000000000;
stap_core_core_core_c0_r1_TL_CFG : DATA + 22'b0000000000000000000000;
stap_core_core_core_c0_r1_TL_STATUS : DATA + 22'b0000000000000000000000;
ALL_CORE_TAPS_3444_PARIR : 2'b00 + DATA;
ALL_CORE_TAPS_3444_PARDR : 1'b0 + DATA + 22'b0000000000000000000000;
} // PADDING
Final IR/DR:
    Scani: 01001110110100
    Scand: 00_00011101
    Scani: 01001110110101
    Scand: 0_1_0000000000000000000000

## Slide 11: Basic Debug approach for Tap
IDCODE.
Overshift.
Write-Read an IR.

## Slide 12: IDCODE:
Each agent has his own “harcoded” code.
  The 1st basic tap babystep is compare this code on tdo.
  STF:
    set SLVIDCODE->DR = 'b00000000000000000000000000000000;
    compare SLVIDCODE->DR = 'b00001110000000000000001010100101;
  ITPP:
    scani: 00100111111000 ;
    scand: 00_00001100, XX_XXXXXXXX ;
    scani: 00100111111001 ;
    scand: 0_00000000000000000000000000000000_0000000000000000000000, X_LLLLHHHLLLLLLLLLLLLLLLHLHLHLLHLH_XXXXXXXXXXXXXXXXXXXXXX ;

## Slide 13: Overshift: (cltap)
Cycle |  |  |  |  |  |  |  |  |  |  |  | BYPASS[0] |  |  |  |  |  |  |  |  | 
0 | X | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 1 |  |  |  |  |  |  |  |  |  | 
1 |  | X | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 1 |  |  |  |  |  |  |  |  | 
2 |  |  | X | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | H |  |  |  |  |  |  |  | 
3 |  |  |  | X | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | L | H |  |  |  |  |  |  | 
4 |  |  |  |  | X | 0 | 1 | 0 | 0 | 1 | 1 | 0 | H | L | H |  |  |  |  |  | 
5 |  |  |  |  |  | X | 0 | 1 | 0 | 0 | 1 | 1 | L | H | L | H |  |  |  |  | 
6 |  |  |  |  |  |  | X | 0 | 1 | 0 | 0 | 1 | H | L | H | L | H |  |  |  | 
7 |  |  |  |  |  |  |  | X | 0 | 1 | 0 | 0 | H | H | L | H | L | H |  |  | 
8 |  |  |  |  |  |  |  |  | X | 0 | 1 | 0 | L | H | H | L | H | L | H |  | 
9 |  |  |  |  |  |  |  |  |  | X | 0 | 1 | L | L | H | H | L | H | L | H | 
10 |  |  |  |  |  |  |  |  |  |  | X | 0 | H | L | L | H | H | L | H | L | H
Formula:
IR_size(0) + Signature.
Signature + IR_size(X)
Final IR/DR:
    Scani: 0100110101
    Scand: HLLHHLHLHX

## Slide 14: Overshift ON TAP LINK(STAP)
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 2'b00 | DATA | 3'b000 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 |  | X | X | X | X | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
After 3 cycles |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 |  |  |  |  | X | X | X |  | X | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  |  |  | 1 | X | X |  | X | X | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 |  |  |  |  |  |  |  |  | L | L | L | L | L | L | H | L | L | L | L | L | L | L | H | X | X | X | X | X | X
Formula:
IR_size(0) +PrePadding(0) + Signature.
Signature + IR_size(X) + PrePadding(X)
Final IR/DR:
    Scani: 0100110101
    Scand: HLLHHLHLHX

## Slide 15: Write-Read:
Same approach as a functional test plan:
  For a randomly selected IR:
    Writes 0x01010101
    Reads 0x01010101
    Writes 0x10101010
    Reads 0x10101010
    Writes Reset value
    Reads Reset value.

## Slide 16: Advance Debug approach for Tap
All this was based on CNL low yield and silicon issues.
  Disable Tap.
  Disable TDO.
  Address Remapping.

## Slide 17: Disable Tap.
Problem:
  All Glue agents listening ALL the time.
What if:
  Some glue agents have the same address but different opcodes?
Result:
  Some agents were being programed with garbage.
Solution:
  Disable the tap via <AGENT>_Config register.
Babystep development:
  Disable the agent via config.
  Read the disable tap on status.
  Read the agent idcode to 0.
DYNAMIC_WR_EN
DYNAMIC_BASE_ADDRESS
DISABLE_WR_EN
DISABLE_TDO
DISABLE_PREVIOUS_LINK_TDO
DISABLE_TAP

## Slide 18: Disable TDO.
Problem:
  All agents connected all the time to tdo.
What if:
  Some agents are throwing garbage to tdo.
Result:
  Even that the agent readout was good,
  the TDO pin was getting mismatches.
Solution:
  Disable the TDO via <AGENT>_Config register.
Babystep development:
  Disable the agent tdo via config.
  Read the disable tdo on status.
  Read the agent idcode to 0.
DYNAMIC_WR_EN
DYNAMIC_BASE_ADDRESS
DISABLE_WR_EN
DISABLE_TDO
DISABLE_PREVIOUS_LINK_TDO
DISABLE_TAP

## Slide 19: Address Remapping.
Problem:
  Agents rely on local address & global address to be accessed.
What if:
  Local and global address are misprogramed
Result:
  Agent basic babysteps were not working with both address
Solution:
  Change the configurable address via <AGENT>_Config register.
Babystep development:
  Change the address into a user defined one.
  Read IDCODE.
  Overshift.
  Write Read to an IR.
DYNAMIC_WR_EN
DYNAMIC_BASE_ADDRESS
DISABLE_WR_EN
DISABLE_TDO
DISABLE_PREVIOUS_LINK_TDO
DISABLE_TAP

## Slide 20: ICXSP taplink net